## Slide 1: GPU Architecture Overview
Patrick Cozzi
University of Pennsylvania
CIS 565 - Fall 2014

## Slide 2: Acknowledgements
CPU slides – Varun Sampath, NVIDIA
GPU slides
  Kayvon Fatahalian, CMU
  Mike Houston, NVIDIA

## Slide 3: CPU and GPU Trends
FLOPS – FLoating-point OPerations per Second
GFLOPS - One billion (109) FLOPS
TFLOPS – 1,000 GFLOPS
Notes: FLOPS are not a perfect measurement because of memory access, instruction mix, branches, etc. Peak FLOPS are idealistic, but not often reached in practice. FMA is one instruction.

## Slide 4: CPU and GPU Trends
Chart from: http://docs.nvidia.com/cuda/cuda-c-programming-guide/
Notes: Moore’s Law – the number of transistors on a chip will double about every two year (not 18 months, that was reference to performance)

## Slide 5: CPU and GPU Trends
Chart from: http://docs.nvidia.com/cuda/cuda-c-programming-guide/
Notes: Moore’s Law – the number of transistors on a chip will double about every two year (not 18 months, that was reference to performance)

## Slide 6: CPU and GPU Trends
Compute
  Intel Core i7: 4 cores – 100 GFLOP
  NVIDIA GTX280: 240 cores – 1 TFLOP
Memory Bandwidth
  Ivy Bridge System Memory: 60 GB/s
  NVIDIA 780 Ti: > 330 GB/s
  PCI-E Gen3: 8 GB/s
Install Base
  Over 400 million CUDA-capable GPUs
Notes: PCI-E Gen3 is 8 GB/s in each direction
2012 CPU: 6-8 core CPU with several MB on-chip cache

## Slide 7: CPU and GPU Trends
Single-core performance slowing since 2003
  Power and heat limits
GPUs delivery higher FLOP per
  Watt
  Dollar
  mm
2012 – GPU peak FLOP about 10x CPU
Notes: See http://www.gotw.ca/publications/concurrency-ddj.htm

## Slide 8: CPU Review
What are the major components in a CPU die?
Notes: Cache, branch predicator, out-of-order logic, ALUs, …

## Slide 9: CPU Review
Desktop Applications
  Lightly threaded
  Lots of branches
  Lots of memory accesses
Profiled with psrun on ENIAC
Slide from Varun Sampath
Notes: Software likes “serial,” hardware likes “parallel.”
Branch prediction accuracy
96.7% - vim
98.9% - ls

## Slide 10: A Simple CPU Core
Image: Penn CIS501
Fetch  Decode  Execute  Memory  Writeback
PC
I$
Register
File
s1
s2
d
D$
+
4
control
Notes: Clocked. All of these steps occur in one clock period.
Clock period bound by datapath delay.
Bad utilization.

## Slide 11: Pipelining
Image: Penn CIS501
PC
Insn
Mem
Register
File
s1
s2
d
Data
Mem
+
4
Tinsn-mem
Tregfile
TALU
Tdata-mem
Tregfile
Tsinglecycle
Notes: About 12-25 gates per-stage, plus 3-5 gates for the latch.
Capitalize on instruction-level parallelism (ILP)
+ Significantly reduced clock period
– Slight latency & area increase (pipeline latches)
? Dependent instructions
? Branches
Alleged Pipeline Lengths:
  Core 2: 14 stages
  Pentium 4 (Prescott): > 20 stages
  Sandy Bridge: in between
Pipelining allows much higher clock speeds.
Pipeline length source: Agner Fog’s Microarchitecture Guide

## Slide 12: Branches
Image: Penn CIS501
jeq loop
???
???
Register
File
S
X
s1
s2
d
Data
Mem
a
d
IR
A
B
IR
O
B
IR
O
D
IR
F/D
D/X
X/M
M/W
nop
Notes: We don’t know what instructions will execute after the branch until the branch is executed. We could either stall until it is, or “speculate” and flush on a misprediction.

## Slide 13: Branch Prediction
+ Modern predictors > 90% accuracy
  Raise performance and energy efficiency
– Area increase
– Potential fetch stage latency increase
Notes:   96.7% accurate on vim example
Flushing a pipeline means a waste of all executed instructions. Area increase potentially even greater for tournament predictors.
Predication avoids explicitly branches completely since the instruction is always fetched and conditionally executed.

## Slide 14: Memory Hierarchy
Memory: the larger it gets, the slower it gets
Rough numbers:
 | Latency | Bandwidth | Size
SRAM (L1, L2, L3) | 1-2ns | 200GBps | 1-20MB
DRAM (memory) | 70ns | 20GBps | 1-20GB
Flash (disk) | 70-90µs | 200MBps | 100-1000GB
HDD (disk) | 10ms | 1-150MBps | 500-3000GB
Notes: SRAM & DRAM latency, and DRAM bandwidth for Sandy Bridge from Lostcircuits
Flash and HDD latencies from AnandTech
Flash and HDD bandwidth from AnandTech Bench
SRAM bandwidth guesstimated.

## Slide 15: Caching
Keep data we need close
Exploit:
  Temporal locality
    Chunk just used likely to be used again soon
  Spatial locality
    Next chunk to use is likely close to previous

## Slide 16: Cache Hierarchy
Hardware-managed
  L1 Instruction/Data caches
  L2 unified cache
  L3 unified cache
Software-managed
  Main memory
  Disk
I$
D$
L2
L3
Main Memory
Disk
(not to scale)
Larger
Faster
Notes: LRU-esque eviction algorithms used for caches. Could be inclusive, exclusive, or neither. OS manages virtual memory.

## Slide 17
Intel Core i7 3960X – 15MB L3 (25% of die). 4-channel Memory Controller, 51.2GB/s total
Source: www.lostcircuits.com
Notes: Look at caches – 24.7% of die is L3 cache – 15MB
32KB I$ and 32KB D$
256KB L2 per core
Memory controller – 15% of die; 4 channels, each supporting DDR3-1600  12.8GB/s

## Slide 18: Improving IPC
IPC (instructions/cycle) bottlenecked at 1 instruction / clock
Superscalar – increase pipeline width
Image: Penn CIS371
Notes: Duplicate pipeline registers, execution resources, ports

## Slide 19: Scheduling
Consider instructions:
xor r1,r2 -> r3
add r3,r4 -> r4
sub r5,r2 -> r3
addi r3,1 -> r1
xor and add are dependent (Read-After-Write, RAW)
sub and addi are dependent (RAW)
xor and sub are not (Write-After-Write, WAW)

## Slide 20: Register Renaming
How about this instead:
xor p1,p2 -> p6
add p6,p4 -> p7
sub p5,p2 -> p8
addi p8,1 -> p9
xor and sub can now execute in parallel

## Slide 21: Out-of-Order Execution
Reordering instructions to maximize throughput
Fetch  Decode  Rename  Dispatch  Issue  Register-Read  Execute  Memory  Writeback  Commit
Reorder Buffer (ROB)
  Keeps track of status for in-flight instructions
Physical Register File (PRF)
Issue Queue/Scheduler
  Chooses next instruction(s) to execute
Notes: New pipeline. 3 Principal data structures.
High power-usage since the fetch/decode logic is always executing – and is not powered down like other FUs.
“dispatch logic scales somewhere between quadratically and exponentially with the issue-width” - http://www.lighterra.com/papers/modernmicroprocessors/

## Slide 22: Parallelism in the CPU
Covered Instruction-Level (ILP) extraction
  Superscalar
  Out-of-order
Data-Level Parallelism (DLP)
  Vectors
Thread-Level Parallelism (TLP)
  Simultaneous Multithreading (SMT)
  Multicore

## Slide 23: Vectors Motivation
for (int i = 0; i < N; i++)
A[i] = B[i] + C[i];
Notes: How do we make this go fast?

## Slide 24: CPU Data-level Parallelism
Single Instruction Multiple Data (SIMD)
  Let’s make the execution unit (ALU) really wide
  Let’s make the registers really wide too
for (int i = 0; i < N; i+= 4) {
// in parallel
A[i] = B[i] + C[i];
A[i+1] = B[i+1] + C[i+1];
A[i+2] = B[i+2] + C[i+2];
A[i+3] = B[i+3] + C[i+3];
}

## Slide 25: Vector Operations in x86
SSE2
  4-wide packed float and packed integer instructions
  Intel Pentium 4 onwards
  AMD Athlon 64 onwards
AVX
  8-wide packed float and packed integer instructions
  Intel Sandy Bridge
  AMD Bulldozer
Notes: Sandy Bridge can issue 2 AVX ops per cycle

## Slide 26: Thread-Level Parallelism
Thread Composition
  Instruction streams
  Private PC, registers, stack
  Shared globals, heap
Created and destroyed by programmer
Scheduled by programmer or by OS

## Slide 27: Simultaneous Multithreading
Instructions can be issued from multiple threads
Requires partitioning of ROB, other buffers
+ Minimal hardware duplication
+ More scheduling freedom for OoO
– Cache and execution resource contention can reduce single-threaded performance
Notes: Register state, return stack buffer, and large page ITLB only replicated stuff: http://www.anandtech.com/show/2594/8

## Slide 28: Multicore
Replicate full pipeline
Sandy Bridge-E: 6 cores
+ Full cores, no resource sharing other than last-level cache
+ Easier way to take advantage of Moore’s Law
– Utilization

## Slide 29: CPU Conclusions
CPU optimized for sequential programming
  Pipelines, branch prediction, superscalar, OoO
  Reduce execution time with high clock speeds and high utilization
Slow memory is a constant problem
Parallelism
  Sandy Bridge-E great for 6-12 active threads
  How about 16K?
Notes: A lot of effort put into improving IPC, and avoiding memory latencies. Attacking throughput is an entirely different game.
GeForce 680GTX – 16K threads

## Slide 30: How did this happen?

## Slide 31: Graphics Workloads
Triangles/vertices and pixels/fragments
Right image from http://http.developer.nvidia.com/GPUGems3/gpugems3_ch14.html

## Slide 32: Early 90s – Pre GPU
Slide from http://s09.idav.ucdavis.edu/talks/01-BPS-SIGGRAPH09-mhouston.pdf
Notes: Wolf 3D – 2.5D. No ceiling and floor height changes (or textures). No rolling walls. No lighting. Enemies always face viewer. Ray casting. Pre-computed texture coordinates.
Doom – Based on BSP tree (Bruce Naylor). Texture mapped all surfaces. Lighting. Varying floor altitudes. Rolling walls.

## Slide 33: Why GPUs?
Graphics workloads are embarrassingly parallel
  Data-parallel
  Pipeline-parallel
CPU and GPU execute in parallel
Hardware: texture filtering, rasterization, etc.

## Slide 34: Data Parallel
Beyond Graphics
  Cloth simulation
  Particle system
  Matrix multiply
Image from: https://plus.google.com/u/0/photos/100838748547881402137/albums/5407605084626995217/5581900335460078306
Notes: Data Parallel – The same program running on multiple data (SPMD).
Cloth is modeled with a mass-spring-damper system obeying Hook’s Law. The force on each mass is computed independently at each time step.
Each particle in a particle system has forces like gravity and wind. Integrating from f = ma to position can be done independently at each time step.
Can an application have more than one type of parallelism?

## Slide 71
Notes: Highlight fixed and programmable components